## Slide 1: Embedded System Laboratory
Lecture 1: Kernel Build, Load & GPIO Control
2020 Summer Training
Made by 許家偉 2020/7

## Slide 2: Outline
Specification of Raspberry Pi 3 Model B+
Implementation
Kernel Building
Boot Procedure
Build Raspberry Pi OS Image
Circuit & Pins
Hands-on Time
Homework
Sincere Blessings

## Slide 3: Specification of Raspberry Pi 3 Model B+

## Slide 4: Specification of Raspberry Pi 3 Model B+

## Slide 5: Implementation
Written in ARM assembly language
  .equ : assigns a value to a symbol , i.e abc .equ 5 , abc now represents five
  ldr : loads from memory
  str : writes to memory
  cmp : compares two values by performing a subtraction. Sets flags.
  b : branch to label
  add : performs arithmetic
Reference: 成大資工 Wiki – ARMv8 , ARM.Reference_Manual.pdf

## Slide 7: Implementation
Base address of GPIO : 0x3f200000
How to access GPIO ?
  SELECT reg. : select GPIO for input/output
  SET reg. : set GPIO for high vol.
  CLEAR reg. : clear GPIO for low vol.

## Slide 8: Implementation
Notes: 看offset就好

## Slide 9: Implementation
Notes: 看offset就好

## Slide 10: Implementation
Notes: 看offset就好

## Slide 11
Notes: .section .init tells the pi where to put the code
.global _start
.equ 增加程式可讀性

## Slide 12: Implementation
ARM linker usually uses 0x8000 to start kernel(OS)
kernel.ld

## Slide 13: Kernel Building
Install arm-none-eabi , The GNU Arm Embedded Toolchain
~$ make

## Slide 14: Boot Procedure
Notes: 首先當我們將板子 power on 後， ARM 的處理器目前是 off 的狀態，而 SDRAM 是 disable 的狀態， 而是利用 GPU 來進行 start booting
GPU 去 ROM 裡執行第 1 階段 bootloader
接著 GPU 又會去 SD 卡中讀 FAT32 第 1 分區的 bootcode.bin (可讀到SD卡會亮綠燈)
bootcode.bin 是第 2 階段 bootloader 他做兩件事
1. enable SDRAM
2. 載入且執行 start.elf
第 3 階段 bootloader 是 start.elf， 讀 kernel image(kernel.img)， configuration 檔 （config.txt）， 和 kernel command line 參數 (cmdline.txt)， 把這些都載入記憶體然後再喚醒 ARM 核心

## Slide 15: Boot Procedure
Format SD card to FAT32 file system
  sudo mkdosfs -F 32 -v /dev/sdd1
  df -Th : list information of disk partition
Copy file into SD card
  bootcode.bin
  start.elf
  kernel.img

## Slide 16: Build Raspberry Pi OS Image
Purpose: get bootcode.bin & start.elf
Download image
unzip 2020-05-27-raspios-buster-lite-armhf.zip
sudo mkdosfs -F 32 -v /dev/sdd1
umount /dev/sdd
dd bs=4M if= 2020-05-27-raspios-buster-lite-armhf.img of=/dev/sdd conv=fsync

## Slide 17: Circuit & Pins

## Slide 18: Hands-on Time

## Slide 19: Homework
摩斯電碼
Make LEDs blink, show the word
“RTES”in Morse code.
Care the time interval (1 time & 3 times)
Write comments
Shorten your code (hint: use macro)
Explain your code

## Slide 20: Sincere blessings