## Slide 1: Embedded System Laboratory
Lecture 2: UART
2020 Summer Training
Made by 許家偉 2020/7

## Slide 2: Outline
Introduction
Implementation
Homework

## Slide 3: Introduction
Universal Asynchronous Receiver Transmitter
All sequence interface transform from Parallel to Serial on transmitter (Tx)
All sequence interface transform from Serial to Parallel on receiver(Rx)
UART provide some status information
  Receiver full or not
  Transmitter empty or not

## Slide 4: Introduction
Microcontroller
Rx
Tx
Device
CPU
Serial input
Parallel output
Serial output
Parallel input
Match baud rate
Match baud rate
UART
Rx full
Tx empty

## Slide 5: Introduction

## Slide 6: Introduction
Serial vs Parallel

## Slide 7: Introduction
Asynchronous vs Synchronous

## Slide 8: Introduction
Baud rate(Speed)
  the unit for symbol rate or modulation rate in symbols per second or pulses per second
Data frame
  Between start bit & stop bit for content
  High for no data/stop bit
  Low for data/start bit
Parity
  detecting errors in transmission
  extra data bit

## Slide 9: Introduction
What is baud-rate
  baud rate gives the frequency at which bits are transmitted on the line
Why we need baud-rate
  no clock is transmitted in asynchronous communication
  the transmitter and receiver must run independently at nearly the same baud rates
A
B
C
D
E
F
G
H
I
J
A B C D E F G I J
Transmitter :
Receiver :
A C E G I

## Slide 10: Introduction
Data frame
Img src: https://developer.electricimp.com/resources/uart

## Slide 11: Introduction
What is odd/even/non parity bit
  the number of bit 1 in an word either even or odd
    even parity : we add a parity bit that number of bit 1 are even
    odd parity : we add a parity bit that number of bit 1 are odd
What is parity bit function
  UART of transmitter will calculate parity bit and send it
  UART of receiver will calculate parity bit from the data it receive
  compare two parity bit are same or not

## Slide 12: Introduction
Example : parity bit
假設傳送 word : 0100 0000
odd parity bit : 0
even parity bit : 1
假設傳送word : 1111 1111
odd parity bit : 1
even parity bit : 0
Example : how to work (odd parity)
Tx
Rx
1110 0110 0

## Slide 13: Implementation
UART in Raspberry 3
  UART0: PL011
  UART1: mini UART
The features of mini UART
  7 or 8 bit operation
  1 start and 1 stop bit
  No parities
  Break generation
  8 symbols deep FIFOs for receive and transmit
  SW controlled RTS, SW readable CTS
  Auto flow control with programmable FIFO level
  16550 like registers
  Baudrate derived from system clock
Notes: 一個是完整功能 PL011 (UART0). 即 Pi 目前內建Linux driver /dev/ttyAMA0

## Slide 14: Implementation
Mini uart Reg.
BCM2837-ARM-Peripherals page 8.

## Slide 15: Implementation
The address of Reg.

## Slide 16: Implementation
Mini uart GPIO

## Slide 17: Implementation
Mini uart GPIO functions
BCM2837-ARM-Peripherals page 102.

## Slide 18: Implementation
Set mini uart GPIO
BCM2837-ARM-Peripherals page 102.

## Slide 19: Implementation – Pull-up/down
not pressed (disconnect), the value read is “0”.
pressed (connect), the value read is “1”.
not pressed (disconnect), the value read is “1”.
pressed (connect), the value read is “0”.

## Slide 20: Implementation – Pull-up/down
BCM2837-ARM-Peripherals page 91, 100.

## Slide 21: Implementation – Pull-up/down
BCM2837-ARM-Peripherals page 101.

## Slide 22: Implementation
Set Baud rate to 115200 bit/s
page 11.

## Slide 23: Implementation
Set AUX_MU_BAUD to 270
page 19.

## Slide 24: Implementation

## Slide 25: Implementation
Set mini uart control & send messages

## Slide 26: Implementation
config.txt
  kernel_old=1 # load kernel from 0x0000
  disable_commandline_tags=1
kernel8.img
  The object code of old kernel.

## Slide 27: Implementation
Circuit & Pins

## Slide 28: Implementation
Terminal on the computer
Download PuTTY

## Slide 29: Implementation
The driver of pl2303HXA
https://www.ez2o.com/Blog/Post/PL2303HX-Win8-Win8.1-Win10

## Slide 30: Homework
終極密碼
  密碼可以自訂 (不用隨機)
Hint:
  utils.S is useful.
Remind:
  Do not modify the following files
  mm.S, linker.ld, config.txt, boot.S, include/mm.h